## Slide 1
A.J. Brown
15 Dec 2025

## Slide 2: Background
Conservation tillage study initiated in 2010
Planned with key farming stakeholders to ensure applicability to real-world scenarios
Data have been collected over the 2011 – 2025 period using multiple methods for water quality and quantity
Overarching goal of investigating the impacts of tillage on runoff water quality, soil health, and agronomic/economic productivity
As of Oct 2025, all water quality, tillage, and crop data have been compiled and merged for research use

## Slide 3: Livin’ on a Layer (of Residue)
Study site in Fort Collins, CO, USA
2011-2025
Conservation Tillage Study started in 2011
  CT = Full tillage
  MT = Less tillage
  ST = Least tillage
Replicated treatment blocks (1 & 2)
Each plot is about 1 hectare with a 300m irrigation run length
Surface irrigated with siphon tube or gated pipe for 7-10 hours at a time

## Slide 4: Diving deeper: Investigating tillage impacts on water quality
Trimarco et al., 2025 found:
Reduced tillage cut particulate pollutant concentrations.
Better soil structure and organic matter aligned with cleaner runoff.
Strip and minimum till performed similarly and both outperformed conventional tillage.
What remains?
Investigation into volume and loadings between treatments over time
Quantifying the actual causal impact of tillage on various analyte concentration and load
Investigating persistence effects of tillage on analytes, if any (unique aspect of these long-term data)

## Slide 5: Proposed Research Objectives*
Characterize treatment differences in water-quality loads through time
  Use the long-term edge-of-field dataset to estimate how sediment and nutrient loads differed among conventional, strip, and minimum tillage, accounting for year-to-year variability and uncertainty in flow and concentration.
Estimate the causal effect of tillage on individual analytes
  Apply hierarchical Bayesian models to isolate the effect of tillage on concentrations and loads for each analyte, separating true treatment signals from measurement error, missing data, and shared temporal structure across analytes.
Identify whether tillage influences persist across years
  Leverage the multi-year record and the multi-output Gaussian process to determine whether tillage effects are short-lived or temporally persistent, evaluating the degree to which past disturbance continues to shape present-year water-quality outcomes.
*These objectives reflect ongoing analyses conducted as part of my Ph. D. research and will contribute directly to my dissertation.

## Slide 6: Problem: Tillage varies in reality
Tillage treatments had fairly standard procedures
  MT = Vertical Tillage + liquid N + banded P
  ST = Strip Tillage + liquid N + banded P
  CT = Moldboard Plow + broadcast N and P
However, some years merit change due to practical considerations
  E.g., VT whole field to prep for wheat planting the day following corn harvest in 2023

## Slide 7: STIR Me Up Before You Go-Go
Soil Tillage Intensity Rating (STIR)
Continuous value that quantifies the overall physical disturbance to the soil caused by a tillage operation
STIR is used in multiple mechanistic models for soil physical impacts (e.g., RUSLE2)
For Kerbel: allows us to account for varying tillage in years where CT/MT/ST treatments were not consistent
Term | Description | Conversion | Notes
Speed [km/h] | Average implement speed | ÷ 1.609 → mph | Converts from km/h to miles per hour
TTM | Tillage Type Modifier [0–1] | none | Represents the aggressiveness of the implement (0 = no till, 1 = full inversion)
Depth [cm] | Average operating depth | ÷ 2.54 → inches | Converts from centimeters to inches
Surf_Disturbance [%] | Percent of soil surface disturbed | ÷ 100 → fraction | Captures the area of soil affected by the implement
STIR | Soil Tillage Intensity Rating | — | Dimensionless intensity index

## Slide 8: Novelty
STIR has never been used as a continuous predictor in a statistical model of observed edge-of-field water-quality concentrations or loads.
Process-based models simulate disturbance directly through mechanistic parameters, so no model links STIR numerically to pollutant export.

## Slide 9: What others do with STIR and why it exists
Used in RUSLE2 and related NRCS tools to represent soil-disturbance intensity that drives predicted erosion and associated sediment-bound nutrient loss (USDA NRCS, 2012; Winger, 2023).
Applied as a management index to classify tillage systems for expected runoff and sediment-loss reductions, not to predict observed water-quality measurements (Ferruzzi, 2023; USDA NRCS, 2022).
Treated as a proxy for residue disturbance and aggregate disruption that influences runoff generation, but rarely modeled against field-measured concentrations or loads (Karlen et al., 2008; Sittig and Sur, 2024).
NRCS uses STIR primarily for:
  Tillage classification
  Conservation compliance thresholds
  Erosion predictions in RUSLE2
  Qualitative links to water-quality benefit
Ferruzzi, G. (2023). Farming Implements in Action: Impacts of Tillage on Soil Disturbance. USDA-NRCS Western Technical Center.
Karlen, D. L., et al. (2008). Soil quality and the RUSLE2 framework for evaluating soil disturbance. Journal of Soil and Water Conservation.
Sittig, N., and Sur, M. (2024). Conservation tillage effects on runoff and erosion: A meta-analysis. Agricultural Water Management.
USDA NRCS (2012). National Agronomy Manual: Residue and Tillage Management Standards 329 and 345.
USDA NRCS (2022). RUSLE2 Operations Database and Soil Tillage Intensity Rating (STIR) Documentation.
Winger, M. (2023). Soil Tillage Intensity Rating training materials. USDA-NRCS.

## Slide 10: STIR Results for Kerbel 2011 - 2025
Chart: Annual STIR Accumulation
Chart: 2011 – 2025 Cumulative STIR
Starting with Tad’s compilation of tillage records as prepared for DayCent (a less robust version of the STIR), I matched these activities (and added 2024 and 2025) to STIR values with assumed tractor speeds from the MOSES (Management Operations and Soil Erosion Simulation) database from NRCS
Snapshot of tillage database

## Slide 11: Problem: Measurement is Hard
Over the years, various methods have been used to collect water quality and quantity
For example:
  Stage measurement: Pressure Transducer, Ruler, Bubbler, and Etape
  Flume type: Weir, 7” V-notch, 8” V-notch, 10” V-notch, and 60° V-Trapezoidal Flume (current)
  Sampler method: GBW, ISCO, GB, LCS, GB3, and GBH
  Analytes have also changed over years
These various methods have varying certainties, which need to be accounted for to harmonize a long-term dataset like this.
Additionally, there are tons of missing data for various reasons related to resource availability for any given year.
TSS comparison example: Our recent, Brown et al., 2025 paper is a great example of trying to account for this in sampler method

## Slide 12: The Times They Are A-Changin’, So Let’s Use a Bayesian Causal Model
Causal models help define a statistical model with scientific assumptions
Statistical models calibrated with Bayesian methods (e.g., Hamiltonian Monte Carlo) provide several advantages
  Imputation of missing data
  Handles small, irregular, and unbalanced data well with informed priors
  Propagates measurement error explicitly
  Models variables jointly, capturing shared correlations for extra ‘horsepower’
  And more!
Thomas Bayes (1761), Presbyterian minister (and statistician) of the Mount Sion chapel in Kent, UK

## Slide 13: Under Pressure… From Confounders
Directed Acyclical Graphs (DAGs) define rules for developing statistical models by following the rules of “do-calculus” i.e., P(y | do(x))
This is where the scientist’s expertise comes in
So, I made one of these for our Kerbel water dataset…
Confounders from (McElreath, 2023)
AJ Agronomy Example
NDVI
Plant Health
Red
NIR
Regress by NDVI OR Red & NIR NOT both

## Slide 15: Model You Like a Hurricane
2 simultaneous models are needed to quantify the direct impact of STIR on load:
  STIR  Volume
  STIR  Concentration
What needs to be included in these regression models?
  STIR, Analyte, Block, Inflow Conc., Irrigation Count, Outflow vol, Sampler Method, Year, duplicate status, flume type
  STIR Only
In Bayes, we can run two models simultaneously to let them learn from each other, and it’s often needed in cases like these – “Full Luxury Bayes”

## Slide 16
Model 1: STIR  Runoff Volume (9845 missing data, i.e., NAs)
Model 2: STIR  Concentration (5599 NAs)
Bonus model: Inflow NA values (9999 NAs)
In Bayes, we can (and should) model missing data as another parameter, resulting in many many parameters like we saw here
is a special parameter called a multi-output Gaussian Process (MOGP).
The MOGP is some fancy matrix algebra that:
Learns a year-to-year trend that all analytes share to some degree (i.e., the “Kernel function”).
Allows each analyte to respond differently to that trend, so they can move together or independently.
Borrows “strength” across analytes and years, improving estimates when data are sparse, missing, or noisy.
Provides realistic uncertainty by modeling temporal variation directly rather than treating it as random noise.

## Slide 17: “Stan” by Me
Run model in R
50 minutes, 0.7 GBs of result
27, 415 parameters fit on 15,366 data points??
  Normal in Bayes 
Model “converges” well!
Stan Software
Rethinking package

## Slide 18: Hit Me With Your Best Plot (Results so far)

## Slide 19: Signed, Sealed, Delivered (It’s STIR)
STIR effects ranked from least to most by analyte type
TDS, TP, TKN, Se, TSP, OP, and TSS were significantly affected
Wider CIs are indicative of fewer data
Results seem to follow theory that insoluble particulates are impacted most, minus OP

## Slide 20: Pump Up the Volume
STIR had a negative impact on volume
This seems contrary to observations and theory. Need to look into this.
Impact is small in magnitude; could be biased by recent MT/ST data

## Slide 21: Load on the Water
Here are the results we want; STIR impacts on LOADS
Fit looks poor b/c it’s averaging over a lot of stuff
Checks out with theory
  TP, TSS, TSP, TKN most affected

## Slide 22: Don’t Stop Decaying
This is the temporal kernel function from the MOGP
Data did change the prior (good)
Posterior shows that there is very little covariance after a single year over all analytes

## Slide 23: Time After Time (But Only for Some Analytes)
So which analytes had temporal effects?
  OP, TP <- clearly
  TSS, TKN <- kinda
This graph represent she ability of a previous year to predict this year’s load

## Slide 24: Yesterday (All My Deviations Seemed So Far Away)
Visualize the actual latent AR(1) trajectories for each analyte
These trajectories show how much real-world year-to-year variability remains after accounting for tillage, sampler, block, and irrigation covariates.
NO3, TKN: A sequence of above-average years around mid-study followed by reversion towards baseline, consistent with the moderate ρ.
TP, TSS: More pronounced multi-year deviations, which is biogeochemically plausible because P and sediment export are tightly linked to cumulative soil surface conditions and disturbance history.

## Slide 25: What’s Left?
Investigate STIR  Volume relationship
Decide on which analytes to present, if not all of them
Produce annual loads by treatment and over cumulative study period with error
Clean some data and re-run the model
  Weird flume labeling, OP merging
Forecast 2026 and compare?
Try machine learning?

## Slide 26: The End
…and in the end, the model you take is equal to the assumptions you make.